## Slide 1
Precise Indoor Localization
(PinLoc*)
*Planned for deployment in Duke’s Nasher Art Museum

## Slide 3
802.11 a/g/n implements OFDM
  Wideband channel divided into subcarriers
  Intel 5300 card exports frequency response per subcarrier
Fingerprinting Wireless Channel
Frequency subcarriers
1 2 3 4 5 6 7 8 9 10 39 48

## Slide 4
Two key hypotheses need to hold:
Temporal
  Channel responses at a given location may vary over time
  However, variations must exhibit a pattern – a signature
1.
Spatial
  Channel responses at different locations need to be different
2.
Is WiFi Channel Amenable to Localization?

## Slide 5
Measured channel response at different times
  Using Intel cards
cluster2
cluster2
cluster1
cluster1
Observe: Frequency responses often clustered at a location
Variation over Time
But not necessarily one cluster per location

## Slide 6
cluster2
cluster2
cluster1
cluster1
2 clusters with different
mean and variance
Variation over Time
Measured channel response at different times
  Using Intel cards
But not necessarily one cluster per location

## Slide 7
Unique clusters per location
How Many Clusters per Location?
Do all 19 clusters occur
with same frequency?

## Slide 8
Most
frequent
cluster
2nd
most
3rd
4th
Others
3 to 4 clusters heavily dominate, need to learn these signatures
Unique clusters per location
Cluster Occurrence Frequency

## Slide 9
Spatial
  Channel responses at different locations need to be different
2.
Clusters with different
mean and variance
Is WiFi Channel Amenable to Localization?
Temporal
  Channel responses at a given location may vary over time
  However, variations must exhibit a pattern – a signature
1.
Location Signature

## Slide 10
What is the Size of a Location?
Localization granularity depends on size
  RSSI changes in orders of several meters (hence, unsuitable)

## Slide 11
Localization granularity depends on size
  RSSI changes in orders of several meters (hence, unsuitable)
Cross correlation with signature at reference location
Channel response changes every 2-3cm
3 cm apart
2 cm apart
What is the Size of a Location?
Define “location” as 2cm x 2cm area, call them pixels

## Slide 12
Will all pixels have unique signatures?
But …
Real (H(f))
Im (H(f))
Self
Similarity
Cross
Similarity
>
Max ( )
Pixel 1
Pixel 2
Pixel 3

## Slide 13
For correct pixel localization:
Self
Similarity
Cross
Similarity
>
Max ( )
0
-
Self – Max (Cross)
AP1
Self – Max (Cross)
AP2
Self – Max (Cross)
AP1 and AP2
67% pixel accuracy even with multiple APs

## Slide 14
Opportunity:
Humans exhibit natural (micro) movements
Likely to hit several nearby pixels
Combine pixel fingerprints into super-fingerprint
67% accuracy inadequate …
can we improve accuracy?

## Slide 15
Intuition: low probability that a set of pixels
will all match well with an incorrect spot
From Pixels to Spots
Combine pixel fingerprints from a 1m x 1m box.
Spot
Pixel
2cm

## Slide 16
Evaluated PinLoc (with existing building WiFi) at:
  Duke museum
  ECE building
  Café (during lunch)
Roomba calibrates
  4m each spot
  Testing next day
  Compare with Horus (best RSSI based scheme)
PinLoc Evaluation

## Slide 17
90% mean accuracy, 6% false positives
WiFi RSSI is not rich enough, performs poorly - 20% accuracy
Accuracy per spot
False positive per spot
Performance