## Slide 1: Smartphone Positioning Systems material from UIUC, Prof. Romit Roy Choudhury

## Slide 2: Motivation
Sudden growth in smartphone industry
  Localization technology caught unprepared
  Industry viewing location as “address” for content delivery

## Slide 3: Motivation
Sudden growth in smartphone industry
  Localization technology caught unprepared
  Industry viewing location as “address” for content delivery
Localization based advertising dollars grew from $12 billion in 2016 to $32 billion in 2021, climbing to 45 percent of overall mobile ad revenue by 2020, reports local marketing and analyst firm BIA Kelsey

## Slide 4
Isn’t today’s technology,
such as GPS, adequate?

## Slide 5: Apps
Information about paintings in museums
Targeted ads in Starbucks, Wal-mart
Access files only from this room
Walking directions in shopping malls
Reminders when passing a library

## Slide 6: Apps
Information about paintings in museums
Targeted ads in Starbucks, Wal-mart
Access files only from this room
Walking directions in shopping malls
Reminders when passing a library
.
.
Information about visible objects (augmented reality)

## Slide 7
207 Coast Road
$7.8M
I wonder how much it costs to live there!

## Slide 8: Enabling Technology
Localization
Apps

## Slide 9: Enabling Technology
Localization
Apps
1. Outdoor Continuous
2. Indoor Semantic
3. High Precision Indoor
4. Object localization

## Slide 10: Enabling Technology
Localization
Apps
1. Outdoor Continuous
2. Indoor Semantic
3. High Precision Indoor
4. Object localization
Constraints
Accuracy
Energy
Calibration
Infrastructure

## Slide 11: Enabling Technology
Localization
Apps
WiFi
Camera
GPS
Inertial / Mag. Sensors
Mic.
1. Outdoor Continuous
2. Indoor Semantic
3. High Precision Indoor
4. Object localization
Constraints
Accuracy
Energy
Calibration
Infrastructure
Hardware
Software

## Slide 12: RADAR: An In-Building RF-based User Location and Tracking System

## Slide 13: The Idea

## Slide 14: Overview
Main Goal:
    Locate/Track users INSIDE a building
Method:
    Recording/Processing signal strength
    Overlapping Coverage  triangulation
Motivation:
    Location aware services/applications

## Slide 15: Previous Work
Focused on IR
    Limited range
    Does not allow for traditional transmitting of data (aka limited to just locating people)
    Scales poorly
    Installation/maintenance limitations
Authors argue that RF solves problems above (range, scalability, deployment, maintenance)

## Slide 16: Methodology

## Slide 17: Building Floor Layout
Figure Notation
    Black Dots = locations where empirical signal strength info was collected
    Large Stars = Base Stations (BS)
    Orientation – North (up); East (right)
Ranges
    Open along hallways w/ base stations (200m)
    Closes elsewhere (25m)
    Base stations overlap in parts and cover the entire floor
      Figure 1: Floor Layout

## Slide 18: Key Idea
Use signal information
    Training Phase
      Construct/validate models for signal propagation
    Real-Time Phase
      Infer location of user

## Slide 19: Data Collection Process for training
Synchronize clocks on mobile host (MH) & BS
MH broadcasts UDP packets
BS records SS at (t, x, y, d)
    Time stamp (t); direction user is facing (d); location (x,y)
    If off-line, user indicates location by clicking map on floor
    Signal strength varies w/i a single location based on d
SS in each of the 4 d’s at 70 (x,y)

## Slide 20: Signal Strength
      Figure 2: Signal strength recorded at the BS as the user walks around the floor.
Why?
    Need accurate SS to help determine location
How?
    Stronger signal = closer to BS
    Modeling (see next slide)

## Slide 21: Model 1: Experimental

## Slide 22: The Empirical Method
Empirical
    Use the data points gathered from training phase to construct search space for NNSS
Nearest Neighbor (NNSS)
    User sends SS and t
    Search previous data for (x,y,d) that corresponds
        assumes user is stationary

## Slide 23: Location Estimate Error
      Figure 3: CDF of error distance for different location methods

## Slide 24: Multiple Nearest Neighbors
Do not limit to just nearest data point (neighbor)
    Expand to k neighbors
      Figure 4: Example of how multiple nearest neighbors can be more accurate (k=3)
May not work well
    Next closest “neighbors” may be same (x,y) but different d
    Small k  <2m change
    Big k  bad estimate
If ignore d, could work for small k, but still not significant enough

## Slide 25: Number of Data Points
      Figure 6: Error Distance as a function of data points
Accuracy of 40 points ~= that of 70 points
Also better if points are uniformly distributed
        x-axis scaled logarithmically

## Slide 26: Mobile User Tracking
4 SS samples/second
Sliding window of 10 samples to compute mean SS
19% worse than that of stationary

## Slide 27: Limitations of Empirical Method
Long time to gather all the empirical data
    1 floor*= (70 locations) · (4 directions) · (20 samples)
    No one wants to collect all that data for a whole office building
If BS moves, have to recollect all the data
~=*1000 square meters

## Slide 28: Model 2: Radio Propagation (theoretical)

## Slide 29: The Radio Propagation Method
Create a search space for NNSS (to be used in the same way as before)
Reduce dependency on empirical data
How?
    Model of indoor signal propagation
    Compute (theoretically) SS data (similar to empirical) for locations (x,y) spaced uniformly along the floor
Performance of method dependent of accuracy of model

## Slide 30: Challenges to Creating Model
Have to account for free-space loss / loss due to obstructions
Multipath Phenomenon
    Signal arrives at user through multiple paths
    Depends on layout of building, construction material, number/type of objects in the building
Each building is different
If a wall (etc) moves, has to be recalculated

## Slide 31: Chosen Model
Floor Attenuation Factor propagation models
    Accommodates different building layouts
    Accounts for large-scale path loss
Adaptations
    Do not care about attenuation due to floors
    Instead focus on walls
        Esp. between transmitter and receiver
        Wall Attenuation Factor (WAF)
Testing “suggests that the entire system can be relocation to a different part of the building, but the same parameter values can be used” (p 9)

## Slide 32: Propagation Model v. Empirical
Not as good as empirical
Better than Strongest BS and Random Methods
      Figure 9: Predicted verses measured signal strength

## Slide 33: Final Thoughts